## Slide 1: R for Environmental Data Analysis
Jory S. Hecht
June 19, 2017
Basin Resilience to Extreme Events
Vermont EPSCoR

## Slide 2: Workshop overview
R Skills
  Introduction to basic data types and commands
  Basic statistical operations
  Programming efficiently with “for loops” and “apply” functions
  Data visualization
  Tips for learning more R on your own
Hydrology/General Data Analysis Skills
  Data cleaning
  Describing streamflow (discharge) variability
  Relating precipitation and streamflow data at different timescales
  Computing extreme floods with given recurrence intervals

## Slide 3: Workshop outline
Basic R data types, objects, and commands
Daily mean discharge time series
Relating daily precipitation to daily mean discharge
Flood frequency analysis

## Slide 4: R background
Developed from S statistical software
Free open-source software used in natural and social science disciplines
Users can create functions and packages
Core group regulates key functions, but extensive user community contributes
Advanced statistical and graphical capabilities
“Hard things are easy, but easy things are hard”
- Common complaint from beginning R users

## Slide 5: Common data types (modes) in R
Data type | Examples
Numeric | 0.54, 3, 4.66
Integer | 1, 2, 3
Logical | TRUE, FALSE
Character | a, b, c

## Slide 6: Dates and times in R
Data type | Examples | Comments
Date | 6/19/2017 | Does not include times
POSIXct (Calendar time) | 6/19/2017 10:00:00 AM EDT | Stored as the number of seconds since the beginning of 1970
POSIXlt (Local time) | 6/19/2017 10:00:00 AM EDT | Stored as a collection of numeric vectors of various time components

## Slide 7: Common types of objects
Object type | Description | Comments
Vector | One dimensional variable | Includes scalars
Matrix | Two-dimensional variable | All columns must have same mode and length
Array | N-dimensional variable | All columns must have same mode and length
Data frame | Two-dimensional dataset, can have different data types | Similar to an Excel spreadsheet, columns must be of equal length
List | Ordered collection of objects | Can contain different object and data types of different lengths
Factor | For nominal (categorical) data | Can order factors on a scale

## Slide 8: Apply functions
Quick way of applying functions across rows and columns
To average across rows:
  apply(TSI,1,mean)
To average across columns:
  apply(TSI,2,mean)
Variations for:
  lists (lapply, sapply)
  subsetting (tapply)
Year | Jul | Aug | Sep | Mean
2012 | 50 | 70 | 70 | 63.3
2013 | 60 | 80 | 60 | 66.7
2014 | 50 | 60 | 40 | 50.0
Mean | 53.3 | 70.0 | 56.7 | 
Hypothetical Trophic State Index (TSI)
TSI > 50  eutrophic

## Slide 9: Array example
Let’s explore different climate and land-use changes with the IAM:
27 Scenarios total (3 x 3 x 3)
Create an empty array to store IAM simulations
Scenarios <- array(NA, dim=c(length(dT),
length(dP),
length(dAg))
 | Future State1 | Future State2 | Future State 3
ΔTemperature (°C) | 0 | 2 | 4
ΔPrecipitation (%) | 80 | 100 | 120
ΔAgricultural Land (%) | 90 | 100 | 110

## Slide 10: USGS streamflow data
The US Geological Survey collects and manages streamflow data at stations throughout U.S.
Data includes continuously recorded discharge estimates
  Measured in ft3/s (cfs) in US (m3/s abroad)
Periodic field measurements establish relation between water level and discharge
We will look at:
  Daily mean discharge
  Annual instantaneous peak discharge
www.researchgate.net

## Slide 11: Missisquoi Bay basin
Extremely high phosphorus loads causes regular algal blooms
Missisquoi River has streamflow gauging station at Swanton (1990-current)
Two precipitation stations at Enosburg cover same period
Must be careful making conclusions with records < 30 years long
Enosburg
Swanton

## Slide 12: Let’s look at the data frame
OPERATOR
STATION ID
DATE
DISCHARGE
DATA QUALITY
Less accurate data

## Slide 13: For loops
One method for running tasks repeatedly
Can be problematic with large data sets
Can state conditions to control looping
Need to create object to store output
For (i in 1:10){
XX[i] <-ifelse(i%%2==0,"even","odd")
}

## Slide 14: Missing data
All days without data in 2017
Provisional data subject to revision
River ice effects could be in play
Provisional data corrected within ~2 years usually

## Slide 15: Water years
In the United States, run from Oct 1 – Sept 30
For instance, Oct 1, 2016 marks the start of WY 2017
Streamflow often reach annual low during late summer/early fall
Chosen for places with winter/spring peaks, summer/early fall recession

## Slide 16: Period-of-record flow duration curves (FDCs)
Flow durations describe how likely a given discharge is exceeded
Assume that flow regime has not changed over time
Many management applications:
  Hydropower
  Ecological assessments
  TMDLs
TMDL for Munroe Brook in Shelburne, VT

## Slide 17: Annual flow duration curves
Describe variability:
  Within years
  Between years
These curves show Q1 to Q99 for each water year
Interannual variability can control many ecological processes
Q1
Q2
Q3
Q99
WY1
WY2
WY3
WYN

## Slide 18
Q1
Q2
Q3
Q99
WY1
WY2
WY3
WYN
Describe variability:
  Within years
  Between years
These curves show Q1 to Q99 for each water year
Interannual variability can control many ecological processes
Annual flow duration curves

## Slide 19: Creating functions
You can create your own functions in R
Let’s code a function that returns the water year for a given date
An R workshop suggests the following function:
WY <- as.numeric(substring(Q_Daily2$Date+92,1,4))
Instead let’s code our own WY_Calc function (back to R script)

## Slide 20: Plot margins in R

## Slide 21: Examining Water Year 1998

## Slide 22
Precip vs. Discharge: Daily vs. annual correlations

## Slide 23: Annual flood series

## Slide 24: Flood frequency analysis
Often want to know annual flood expected every 1 in T years on average (e.g. 100-year flood)
Annual flood of a percentile p is exceeded 1/(1-p) years
Must make sure watershed conditions are not undergoing long-term change
Lognormal distribution often fits well, related to normal distribution
Official distribution throughout United States is Log-Pearson Type III (LP3)
For p = 0.90, = 1.281

## Slide 25: Annual flood series
Be careful with extrapolation beyond flood of record

## Slide 26: How to learn more R
Help within R (look at examples!)
Free online courses (e.g. Coursera)
Extensive online documentation
  Quick-R
Participate in online forums
  StackOverflow
  Subscribe to blogs and other alerts
Network with users in your research areas
Give a tutorial or workshop to peers!

## Slide 27: Thank you!
Happy to help you learn R:
  Training on trend analysis and distribution fitting (TBD)
  Graphics for posters (consider using ggplot2 package)
Materials will be on my Github site
E-mail me at jory.hecht@uvm.edu